General info and limitations

# Weather limitations
Weather minimums for landing
Approach mode	Minimums
	Decision height, m	Visibility, m
Automatic approach	30	350
Directors / ILS CatIII	60	550
ILS	100	1200
By two ADF	120	1800
By one ADF	250	4000
Visual approach	210	4000

Maximum wind
On taxi and pushback	30 m/s;
Wind limits on take-off and landing:
- headwind	30 m/s;
- tailwind	10 m/s;
- side wind 90° to runway:
- normal conditions	17 m/s;
- failure of two hydraulic systems	10 m/s;
- precipitation:
- if water level is under 3mm – see the table below
- if water lever above 3mm	5 м/с.
Maximum side wind
Runway friction coeficient	0.3	0.4	0.5	0.6+
Maximum side wind part, m/s	5	11	17	17

Maximal flight altitude
Flight level	11100 m / 36500 ft	11600 m / 38000 ft	12100 m / 39700 ft
Maximum gross weight, kg	No limits	93500	85000

# General flight limitations

Gross weight limits
Maximum taxi weight………. ………………………………………………………...100,5 t.
Maximum take-off weight……………………………………………………………… 100 t.
Maximum landing weight……….. ………………………………………………………80 t.
Maximum zero fuel weight…………………. …………………………………………...74 t.
Maximum commercial load……………. ………………………………………………...18 t.

CG limitations
Maximum forward CG position on take-off, LG extended…………………. ………21 % MAC.
Maximum forward CG position on landing, LG extended …………………………..18 % MAC.
Maximum back CG position, LG retracted:
(а) normal flight…………………… ………………………………………………..32 % MAC;
(б) if take-ff weight is less than 80 t and flightlevel is under 330, Autopilot works only in manual mode and commercial load doesn't allow to reach 32% MAC CG position, then it is allowed to fly with CG position up to 40% MAC.
CG for tail overturn on ground.………………………...………………………….52,5 % MAC.

Maximum G-overloads
Maximum G load for any weight
- flaps retracted……………………………………………………………….………. 2.5
- flaps extended………………..…………………………………….………………... 2.0
Minimum G load for any weight
- flaps retracted…………………………………………………………….…………. 0.0
- flaps extended………………………………………………………………...……... 0.2

Maximum bank angle
When maneuvering under 250m altitude or airspeed less than 340 km/h on takeoff and less than 280 km/h on landing………………………………………………………………………. 15°
Extending and retracting flaps…… …………………………………………………...25°
All other situations……………………………………………………………………..30°
# Speed limits
Maximum operation speed (V мо) and М number (М мо):
- with CG position 32% MAC and less:
- on altitudes less than 7000 m ...........................................................……..……600 km/h;
- on altitudes more than 7000 m ............................................….…….. 575 km/h, М = 0,86.
- with CG position more than 32% MAC .........................….........……………..... 525 km/h.
Maximum speed V max and М mах:
- on altitudes less than 7000 m ...........................................................…......... 650 km/h;
- on altitudes more than 7000 m and less than 10300 m .................................. 625 km/h;
- on altitudes > 10300 m .................................................................................... М = 0,95.
Maximum airspeed with yaw or roll damper failure ..............……...525 km/h, М = 0,85.
Maximum speed with flaps, extended to angle:
- 15° .................................................................................................................. 420 km/h;
- 28° .................................................................................................................. 360 km/h;
- 36° .................................................................................................................. 330 km/h;
- 45° .................................................................................................................. 300 km/h.
While retracting flaps from 15° to 0° it is allowed to reach speed 430 km/h.
Maximum landing gear operating speed:
- in normal conditions .....................................................………......................... 400 km/h;
Maximum speed for flight with non-flight stabilizer position.............................. 450 km/h.
Maximum speed for operating stabilizer ...……………………………….......... 425 km/h.
When take-off or go-around, while stabilizer moves to in-flight position……... 450 km/h,.
Maximum speed with slats extended…………………………….. ............……..425 km/h.
While slats retracts, it is allowed to speed up to............................................….... 450 km/h.
Maximum speed to operate landing lights……….. ........................................…...400 km/h

Maximum groundspeed:
- rising nose-wheel (rotate) ..............................................................……………... 315 km/h
- take-off main gears…………... ..................................................................…...... 325 km/h
- touchdown main gears………………. .......................................................…….. 280 km/h
- touchdown nose-wheel…………. ............................................................…….... 270 km/h
- start using brakes when air temperature is:
- +30 °С and below.................................................…..............................…..……. 240 km/h
- more than +30 °С ...........................................................................................…... 225 km/h

# Synchronized stabilizer positions
Aircraft configuration	Flaps angle, deg	Slats position	CG position %MAC
			Less than 24	24-32	More than 32
			Stab setting
			F / green / color	M / black / color	B / yellow / color
			Stabilizer position, deg
Flight	0	Retracted	0	0	0
Take-off	15, 28	Extended	3	1.5	0
Landing	36, 45	Extended	5.5	3	0

# Aircraft configuration on each flight stage
Take-off:
- flaps extended to 15° or 28°,
- slats extended;
- stabilizer in sync position;
- spoilers retracted;
- landing gear deployed.
In flight:
- flaps retracted;
- slats retracted;
- stabilizer in flight position (0°);
- spoilers retracted (may be extended on descend);
- landing gears retracted.
Emergency descend:
- flaps retracted;
- slats retracted;
- stabilizer in flight position (0°);
- middle spoilers extended;
- landing gear deployed.
On landing:
- flaps:
- in normal conditions extended to 45° or 36°,
- when landing with two working engines, extended to 36°;
- when landing with one engine, extended to 15°;
- slats extended;
- stabilizer synchronized, see table above;
- middle and inner spoilers deploys automatically on touchdown;
- landing gears deployed.

# Take-off speeds
Flaps 28°
Weight, t	70	75	80	85	90	95	100
V1, km/h	205	210	220	230	235	240	250
Vr, km/h	215	220	230	240	245	250	260
V2, km/h	235	245	250	260	270	275	280
V flaps to 15°, km/h	Not less than 330
V flaps to 0°, km/h	Not less than 360						365

Flaps 15°
Weight, t	70	75	80	85	90	95	100
V1, km/h	220	230	235	245	250	260	270
Vr, km/h	230	240	245	255	260	270	280
V2, km/h	270	280	285	295	305	315	320
V flaps to 0°, km/h	Not less than 360						365

# Approach speeds
Weight, t	60	65	70	75	80	85	90
Flaps 0°, slats 0°	318	332	344	356	368	380	401
Flaps 0°	295	307	317	328	340	351	361
Flaps 15°	251	261	270	280	288	297	305
Flaps 28°	236	247	255	265	273	282	288
Flaps 36°	232	242	250	260	268	276	283
Flaps 45°	230	240	247	257	265	272	280